## Slide 1: Vivado Design Flow
Zynq
Vivado 2015.2 Version

## Slide 2: Objectives
After completing this module, you will be able to:
  Explain how the design analysis features of the Vivado IDE can help in FPGA design development
  List the main features of the Vivado IDE
  Describe the Vivado IDE Design flow
  Introduce the scripted Vivado IDE design flows

## Slide 3: Outline
Vivado IDE Features and Benefits
Vivado Design Suite Introduction
Vivado Design Flow
Summary

## Slide 4: Vivado IDE Solution
Interactive design and analysis
  Timing analysis, connectivity, resource utilization, timing constraint analysis, and entry
RTL development and analysis
  Elaboration of HDL
  Hierarchical exploration
  Schematic generation
XSIM simulator integration
Synthesis and implementation in one package
I/O pin planning
  Interactive rule-based I/O assignment

## Slide 5: Who Should Use Vivado?
Designers needing an interactive design approach
  Analysis and area constraints to drive place & route
Challenging designs
  Large devices, complex constraints, and high device utilization
  Advantages are also seen with small devices
Designs experiencing implementation issues
  Performance, capacity, run time, and repeatability
Designs requiring implementation control
  Users looking for options other than just a pushbutton flow
  Visualize design issues from many aspects
  Block-based design constraints
Designs targeting the 7-Series (or newer) devices
Notes: Typical designers are involved in complex, high-density designs. They do not mind using a more interactive and iterative approach, as opposed to a pushbutton flow (as long as it produces improved timing results). Vivado IDE users also include those who want to be more involved (in control) of what the implementation tools are doing.
The productivity gains enabled by the Vivado IDE will help reduce the overall implementation iterations required by these types of designs.
Typical designers need extra performance and have experienced implementation issues previously.
Often, complex designs require many iterations to finalize the performance. This is because designers run the risk of not meeting their timing with each iteration when running implementation on the entire design. The use of area constraints can improve the consistency of your timing results, although it does not guarantee meeting your timing objectives.

## Slide 6: Vivado’s Visualization Feature
Visualize and debug your design at any flow stage
  Cross-probing between netlist/schematic/RTL

## Slide 7: Gain Faster Timing Closure
Analyze multiple implementation results
  Highlight failing timing paths from post-route timing analysis
  Quickly identify and constrain critical path logic
Hierarchical floorplanning
  Guide place & route toward better results
Utilization estimates
  All resource types shown for each Pblock
  Clocks or carry chains
Connectivity display
  I/Os, net bundles, clock domains
Notes: The Vivado IDE provides a comprehensive environment for analyzing timing issues and easily constraining timing-critical logic to improve performance. Results can be used to plan a floorplan of the design by determining what logic should be grouped together and where it should placed on the die. When timing-critical logic is grouped closer together, the implementation tools can use faster routing resources to improve timing.
Grouping logic is performed with physical blocks (called Pblocks) by selecting logic in a variety of different ways.
The Vivado IDE also provides resource utilization estimates to help size any Pblocks. These same statistics report clock information, carry chain size, and a variety of other useful information.
The Vivado IDE provides excellent insight into the design by displaying I/O interconnect as well as Pblock net bundles. Inter-Pblock net bundles change color and size depending on the number of signals shared by Pblocks. This makes it easy to see heavily connected Pblocks and the data flow through the FPGA. Designers can then take corrective action to place heavily connected Pblocks closer or merge them into one Pblock.

## Slide 8: Tcl Capability
Tcl Console enables the designer to actively query the design netlist
Full Tcl scripting support in two design flows
  Project-based design flow provides easy project management by the Vivado IDE
  Non-project batch design flow enables entire flow to be executed in memory
Journal and log files can be used for script construction

## Slide 9: Project Based vs Non-Project Batch Flows
Vivado tools support two flows
  Project based
  Non-project batch
Non-project batch flow
  No project infrastructure
  Tcl based
  Can use GUI for visualization via the start_gui command
  Must manually create reports and checkpoints via commands
Project-based flow
  Project infrastructure is saved in *.XPR file
  Reports/state/runs/cross-probing is available
  IDE GUI or Tcl script both available

## Slide 10: Outline
Vivado IDE Features and Benefits
Vivado Design Suite Introduction
Vivado Design Flow
Summary

## Slide 11: Typical vs Vivado Design Flow
Interactive IP plug-n-play environment
  AXI4, IP_XACT
Common constraint language (XDC) throughout flow
  Apply constraints at any stage
Reporting at any stage
  Robust Tcl API
Common data model throughout the flow
  “In memory” model improves speed
  Generate reports at all stages
Save checkpoint designs at any stage
  Netlist, constraints, place and route results
Notes: synth_design is normal except that it now can read in XDC constraints into synthesis. The Vivado IDE includes a timing-driven synthesis tool that uses a common constraint language throughout the flow. From synthesis all the way through place and route.
Netlist linking is done in link_design. Here if you do have third-party EDF, the files can be read into the Vivado IDE.
opt_design, power_opt_design, and place_design are the packing and placement functions. power_opt_design is optional, however.
phys_opt_design is also optional. The significant thing is that all of data is stored in one data model.
You can run that entire flow in memory and never write anything files out when using the non-project batch design flow. But in any flow there is no data translation, no data model. There are huge advantages to that in terms of speed. Checkpoints can be saved at any stage of the design flow when using the non-project batch design flow. A checkpoint is basically a snapshot of your design in time. All of these commands can be scripted, so the flow is very flexible.
The single data model in memory allows you to do a lot of things, such as cross-probing and fixing your timing at the end of the implementation without having to reimplement again.

## Slide 12: Design Database
Processes access the underlying database of your design
  Each process operates on a netlist and will modify the netlist or create a new netlist
Different netlists are used throughout the design process
  Elaborated
  Synthesized
  Implemented

## Slide 13: What is a Netlist?
A Netlist is a description of your design
  Consists of cells, pins, port and nets
  Cells are design objects
    Instances of user modules/entities
    Instances of library Basic Elements (BELs)
      LUTs, FF, RAMs, DSP cells, etc…
    Generic technology representations of hardware functions
    Black boxes
  Pins are connection points on cells
  Ports are the top level ports of your design
  Nets make connections between pins and from pins to ports

## Slide 14: Netlist Objects
Notes: Ports are the primary inputs and outputs of the current design (normally the top level module).
Pins are the connections to instances – both instantiations of hierarchical objects and primitive cells.

## Slide 15: Elaborated Design
Representation of the design before synthesis
  Interconnected netlist of hierarchical and generic technology cells
    Instances of modules/entities
    Generic technology representations of hardware components
      AND, OR, buffer, multiplexers, adders, comparators, etc…

## Slide 16: Object Names in Elaborated Design
Object names are extracted from RTL
  Instance and pin names of hierarchical objects
  Inferred flip-flops from underlying reg/signal/logic
    Suffix _reg is added
  Nets from underlying reg/signal/logic when it makes sense

## Slide 17: Synthesized Design
Representation of the design after synthesis
  Interconnected netlist of hierarchical and Basic Elements (BELs)
    Instances of modules/entities
    BELs
      LUTs, flip-flops, carry chain elements, wide MUXes
      Block RAMs, DSP cells
      Clocking elements (BUFG, BUFR, MMCM, …)
      I/O elements (IBUF, OBUF, I/O flip-flops)
Object names are the same as names in the elaborated netlist when possible

## Slide 18: Implemented Design
Representation of the design during and after the implementation process
  Structurally similar to the Synthesized Design
  Cells have locations, and nets are mapped to specific routing channels

## Slide 19: Project Data
All project data is stored in a project_name directory containing the following basic set of directories:
  project_name.xpr file: Vivado project file, contains project settings
  project_name.runs directory: Contains all run data
  project_name.srcs directory: Contains all imported local HDL source files, netlists, and XDC files
  project_name.data directory: Stores floorplan and netlist data

## Slide 20: Journal and Log Files
Journal file (vivado.jou)
  Contains just the Tcl commands executed by the Vivado IDE
Log file (vivado.log)
  Contains all messages produced by the Vivado IDE, including Tcl commands and results, info/warning/error messages, etc.
Location
  Linux: directory where the Vivado IDE is invoked
  Windows via icon: %APPDATA%\Xilinx\Vivado or C:\Users\<user_name>\AppData\Roaming\Xilinx\Vivado
  Windows via command line: directory where the Vivado IDE is invoked
  From the GUI
    Select File > Open Log File
    Select File > Open Journal File

## Slide 21: Checkpoints
Saves the database from memory to disk
  Netlist – edif (eventually a Verilog netlist)
  Constraints – xdc
  Placement/routing/config db – xdef
Tcl commands
  write_checkpoint <filename>
    Results in a filename.dcp file, which is a compressed file
    Can unzip this file if needed: filename.edf, filename.xdc, filename.xdef, filename.wdf, and dcp.xml
  read_checkpoint <filename>
Can read and write in the IDE as well
  When read in gives a project-less setup
Can open and modify checkpoints in IDE

## Slide 22: Outline
Vivado IDE Features and Benefits
Vivado Design Suite Introduction
Vivado Design Flow
Summary

## Slide 23: Getting Started Jump Page
All buttons grouped by functionality
Quick Start
  Previous projects can quickly opened
  Links to create new or example projects
Tasks
  IP management, hardware manager, Tcl Store
Helpful links
  Documentation and Tutorials
    Invokes PDF viewer for documentation
  Quick Take Videos
  Release Notes Guide
Tcl Console for command line access

## Slide 24: New Project Creation Wizard
Very first step is project creation with five choices
Five different types of projects:
  RTL
    Front-to-back (even for Block Designs)
  Post-synthesis
    EDIF or NGC
  I/O planning
    For early pin testing
    No design sources
  Import Project
    Imports existing project from Synplify, XST, or ISE
  Example Project
Notes: RTL Project:
The RTL Project environment enables analysis of the compiled RTL design including logic exploration, resource and power estimation, DRCs, and I/O pin planning.
Post-synthesis Project:
This is where pre-implementation design analysis, debug core insertion, and constraint definition is performed. You can explore various constraints sets, devices, and implementation options.
Import ISE tool results:
The Implemented Design environment loads the netlist and implementation results directly from the run directory to ensure that the viewed data represents the launched run.

## Slide 25: Project creation flow (RTL/Synthesized Design)
Defines the project name and location
Select source files in RTL project creation
  All recognized source files, Verilog, VHDL, in the directory and subdirectories, can be added
Select post-synthesized netlist in Post-synthesized project creation
  All synthesized files in the directory and subdirectories, are added
Select constraint files
  One or more constraints files including IP specific and top-level can be added
Select target device or pre-defined board
Reference original existing files or import and copy them into the project

## Slide 26: Constraints File Management
Constraint sets are a collection of XDC files
  A project can contain multiple constraint sets
  For a constraints set to be applied, it must be set to "active"
    Any constraint set can be made active by right-clicking and selecting Make Active
Target XDC
  The XDC file in a constraint set to which new constraints are written
    From the Constraints Wizard for example
  Target XDC can be specified by right-clicking and selecting Set As Target Constraint File

## Slide 27: Project Navigator
Used to manage sources, customize IP, and view project details in the Project Summary
Flow Navigator
Sources view
  Hierarchical display of sources, including constraints files
  IP Sources and Libraries view
    HDL and netlists including references to library and location
Project Summary
  Gives access to device utilization (resources), timing summary, and strategy information
Tcl Console, Messages, Compilation, Reports, and Design Runs

## Slide 28: Project Settings
General settings
  Select device
  Target HDL language
  Simulation tool (Vivado simulator included)
  Top module name
  Language options

## Slide 29: Flow Navigator – RTL Project
Configure project sources
  Add HDL source files, constraints files, simulation files, block designs
IP Integrator
  Create, open, generate a block design
Run Simulation
  XSIM simulator included
  Behavioral, post-synthesis, post-implementation
RTL Analysis
  Open Elaborated Design button: Loads the elaborated RTL design

## Slide 30: Flow Navigator – RTL Project, cont’d…
Run Synthesis
  Timing driven
  Open Synthesized Design button: Loads synthesized netlist
Run Implement button: Runs implementation tools
  link, opt, power_opt, place, phys_opt, and route
  Open Implemented Design button: Loads implemented design
Program and Debug: Launches programming and debugging tools
  Open Hardware Manager to program the FPGA
  Hardware Manager also contains debug capabilities

## Slide 31: Simulation
The Vivado simulator, XSIM, supports RTL, netlist, and timing simulation
Part of the Vivado installation

## Slide 32: Adding Testbench Files
Testbench sources (*.V or *.VHD) must be added separately from design sources
  In the Flow Navigator, click Add Sources
  Select Add or Create Simulation Sources option and click Next
  Click on the Green + button, add files…, add directories… if the testbench file is already available or click on Create File… button to create a new testbench file
  Select a file type- Verilog, Verilog Header, SystemVerilog, or VHDL
  Browse to an existing testbench or enter a filename to create

## Slide 33: Simulation Settings
Allows selection of compilation and simulation properties
  From the Flow Navigator, click Simulation Settings
  The simulation top module is the testbench you have written and specify
  Additional options can be entered
    More Compilation Options field under Compilation tab
    More Simulation Options field under Simulation tab
Refer to the Vivado Design Suite Simulation Guide (UG900) for more information

## Slide 34: Simulation Results
Graphical waveform display
Toolbar buttons for adding markers, measuring delays, and zooming
Buses can be expanded to view individual signals
Dividers can be inserted to visually isolate groups of related signals
Console displays any messages output from testbench
By default, the top-level signals are displayed

## Slide 35: After Elaboration
Sources, RTL Netlist, and Device Constraints tabs available
Properties of selected items
Generate DRC and Noise reports
RTL Schematic View
Views can be selected by purpose
  Clock Planning
  I/O Planning
  Floorplanning
Notes: After you have elaborated the design, the Project Manager appears. Note that the Flow Navigator has changed (note the new options under RTL Analysis). The figure shows the RTL Schematic layout, but other views can be selected.
RTL Netlist window: Shows a name for each primitive in the design.
As each is selected, the Instance Properties view shows specific details. Physical constraints: list Pblocks associated with the design. Device view: Shows the specific resources on the die that are selected. It also shows location constraints (LOCs) and range assignments on Pblock.

## Slide 36: After Synthesis
The Flow Navigator includes access to Constraints Wizard, Edit Timing Constraints, Set Up Debug, Report Timing Summary, Report Clock Networks, Report Clock Interaction, Report DRC, Report Noise, Report Utilization, Report Power, and Schematic utilities
The schematic view will be opened including input/output buffers
Views can selected by purpose
  I/O Planning, Clock Planning, Floorplanning, Debug, Timing Analysis
    All timing information is only an estimate (until implementation has completed)

## Slide 37: After Implementation
Sources and Netlist tabs do not change
  As each resources in the Netlist tab is selected, it will show the exact placement of the resource on the die in the Device view
  As each path is selected, the placement of the logic and its connections is shown in the Device view
  This is the cross-probing feature that helps with static timing analysis
Views can selected by purpose
  I/O Planning, Clock Planning, Floorplanning, Timing Analysis
Access to Constraints Wizard
Timing results have to be generated with the Report Timing Summary

## Slide 38: Outline
Vivado IDE Features and Benefits
Vivado Design Suite Introduction
Vivado Design Flow
Summary

## Slide 39: Summary
Features and benefits of the Vivado IDE include
  Improved performance and device utilization with the use of Pblocks and area constraints
  Performance predictability
  Design analysis features that speed a designer's ability to gain timing closure Tcl features (commands) that make scripting easier and powerful
Vivado tools use a common data model throughout the FPGA design process
  This yields runtime and memory resource benefits to the user
Vivado tools support scripting in non-project batch and project-based design flows
  Vivado tools support the use of Tcl for all commands
Vivado tools use a common constraint language (XDC) throughout the design process
  This enables synthesis optimization significantly better than the ISE software
Pushbutton flows for most designs
Advanced tools for challenging designs