## Slide 1: Lab1 Intro Intro to Partial Reconfiguration Flow
Zynq
Vivado 2015.2 Version

## Slide 2: Outline
Objectives
The Design
Methodology
Summary

## Slide 3: Objectives
After going through this lab, you should be able to:
  Use Tcl script to generate a Vivado IPI design, create a wrapper file from it, add the static logic files and generate the design checkpoint
  Use Vivado’s bottom-up methodology to synthesize the necessary RMs
  Floorplan the design
  Add the desired RMs
  Create multiple configurations
  Implement the design and generate full and partial bitstreams for various configurations
  Download bitstreams to demonstrate a working partial reconfigurable design

## Slide 4: Outline
Objectives
The Design
Methodology
Summary

## Slide 5: The Design
Source files consist of HDL (Verilog) files
Two RPs, each with two RMs
One RP performs addition and subtraction option
Other RP performs right- and left- shifting function as evident from LEDs display

## Slide 6: The Design
Static logic consists of UART receiver and transmitter, command parser, and LED control modules
Serial communication at 115200 Baud
Button_stop stops shifting, Buttons_start starts shifting pattern, and reset button resets the system
The PS system is used to move receive and transmit data between the external USB-UART bridge and the internal signals to PL

## Slide 7: The Design – Directory Structure
The home directory of the lab contains Tcl scripts to generate the initial design and synthesize the RMs
Bitstreams will hold the generated full and partial bitstreams
Checkpoint will hold various design snapshots during the flow
Implement contains various configuration directories and associated results will be placed into those sub-directories
Synth is where RMs’ and the static design checkpoints (netlists) are stored
The BOOT directory under the Sources directory has the BOOT.bin file which is needed for the board to boot from. It brings the UART pins of the PS to the PL side. This is done through a software application provided in the uart_through_gpio.sdk folder
The hd_visual directory will have several script files which can be used to visualize the routing and placement

## Slide 8: Outline
Objectives
The Design
Methodology
Summary

## Slide 9: Methodology
Create a Vivado project
  Generate design checkpoint for the static design in Vivado IDE
Synthesize each RM separately
  Generate RM checkpoints for each RM through script using out of context synthesis
    Each RM residing in a same RP must have same number, type, and size ports and the top-level module (entity) name
    The out of context synthesis won’t insert I/O buffers
Define Reconfigurable Partitions pblocks
  Bring reconfigurable partitions as black boxes
  A design may have one or more reconfigurable partitions
  Define the black boxes as reconfigurable partitions
    Set HD.RECONFIGURABLE
    PR feature should have been licensed

## Slide 10: Methodology
Add Reconfigurable Modules
  For each RP, add reconfigurable modules by providing unique name and unique netlist file
    The netlist file will typically be a flat design (rather than hierarchical)
Define Reconfigurable Partition area
  Use Draw Pblock
  The drawn area should be large enough to provide the required types and amount of resources
  This design uses slices resources

## Slide 11: Set Pblock Size
Find sites using Edit -> Find command
Mark locations
Draw pblock

## Slide 12: Methodology
Run Design Rule Checker (DRC)
  The DRC checks for violations in floorplanning, clocking regions, IOs, partial reconfiguration specific
Create first configuration using one RM from each RP
  Add top-level I/O if necessary
  Run Implementation using default options
    Implements static and the two RPs
Replace the used RMs with the blackboxes and save the design checkpoint
  So the design checkpoint can be used in subsequent configurations
Create additional configurations
  Since we have 2 RPs and 2 RMs in each RP, we can have up to eight possible configurations including blank RP
  Minimum required will be three which provides all possible partial bitstreams, importing static region results from the first configuration

## Slide 13: Methodology
Run PR_Verify
  To ensure that the static implementation, including interfaces to reconfigurable regions, is consistent across all Configurations
Generate bitstreams
  Minimum of one full bitstream is necessary
  Must have partial bitstream for each RM
  Optionally generate blanking bitstreams for each RP
    Blanking bitstreams can be used to clear the region logic when the functionality in that region is not being used for a while, possibly reducing power consumption
Verify the design

## Slide 14: Outline
Objectives
The Design
Methodology
Summary

## Slide 15: Summary
This lab showed you steps involved in generating partial reconfiguration design using Vivado 2015.2 with partial reconfiguration feature enabled. You used the provided Tcl scripts to generate the static design that consists of the processing system to configure the UART port as a simple GPIO port and extend the signals to the programmable logic sub-system where they are connected to the actual design. You used another script to synthesize the RMs in a bottom-up approach which is required for the PR flow. You created the configurations and implemented the design. You generated the full and partial bitstreams, downloaded them and verified the functionality using the development board.