## Slide 1: Introduction to Partial Reconfiguration Methodology
Zynq
Vivado 2015.2 Version

## Slide 2: Objectives
After completing this module, you will be able to:
  Define Partial Reconfiguration technology
  List common applications for using Partial Reconfiguration
  Define Partial Reconfiguration terminology
  State the Partial Reconfiguration flow

## Slide 3: Outline
What is Partial Reconfiguration(PR)?
PR Technology
PR Terminology
PR Design Flow
Summary

## Slide 4: What is Partial Reconfiguration?
Configuration Port or ICAP
Configuration Port
Partial Reconfiguration is the ability to dynamically modify blocks of logic by downloading partial bit files while the remaining logic continues to operate without interruption.
Full
Bit File
Partial Bit Files
Function A1
Function B1
Function C1
Function C2
Function B2
Function A2
Function A3

## Slide 5: PR Applications Analogy
Process 1
Processor Context Switch
Process 2
Partial Bitstream A
FPGA
FPGA Configuration Switch
MMU
Stack
PR region 1
PR region 2
PR region N
uP
Process N
Partial Bitstream B
Partial Bitstream N

## Slide 6: PR Applications Analogy
Process 1
Processor Context Switch
Process 2
Partial Bitstream A
FPGA
FPGA Configuration Switch
MMU
Stack
PR region 1
PR region 2
PR region N
uP
Process N
Partial Bitstream B
Partial Bitstream N
Notes: A FPGAs PR region is similar to the stack in a microprocessor. The FPGA can have many PR regions so it can be much more powerful than a microprocessor for applications switching.

## Slide 7: Partial Reconfiguration Technology and Benefits
Partial Reconfiguration enables:
  System Flexibility
    Swap functions and perform remote updates while system is operational
  Size and Cost Reduction
    Time-multiplexing hardware requires a smaller FPGA
    Reduces board space
    Minimizes bitstream storage
  Power Reduction
    Via smaller or/and fewer devices
    Swap out power-hungry tasks

## Slide 8: System Flexibility: Communication Hub
The FPGA can be a communications hub and must remain active
  Cannot perform full reconfiguration due to established links
FPGA
PR region 1
PR region 2
PR region 3
Radio Link
Monitor
Video
Link
Bus Link

## Slide 9: Size and Cost Reduction: Time Multiplexing
Applications need to be able handle a variety of functions
  Supporting many at once can use a great deal of space
The library of functions use case covers a wide number of applications
  Time-based multiplexing of functions reduces device size requirement
Notes: A software-defined radio is an example.

## Slide 10: Power Reduction Techniques with PR
Board space and resources are limited
  Multi-chip solutions consume extra area, cost, and power
Many techniques can be employed to reduce power
  Swap out high-power functions for low-power functions when maximum performance is not required
  Swap out black boxes for inactive regions
  Swap high-power I/O standards for lower-power I/O when specific characteristics are not needed
  Time-multiplexing functions will reduce power by reducing amount of configured logic

## Slide 11: Customer Example Flexible Video Processing
Swap decoders on the fly
  One channel remains up while the other changes
Released “flat” version first
  Two decoders per channel
Expanded functionality without changing hardware
  Deployed new bitstreams for more decoders without changing hardware
Display
Output
Decoder
[MPEG2, DV, VC3, ProRes 422]
Data Decode Scheduler
Data Input
DDR2 Memory
Controller
64 bits @ 250 MHz DDR2
32 bits @ 125 MHz
128 bit @ 250 MHz
128 bit @ 250 MHz
128 bit @ 250 MHz
128 bit @ 250 MHz
10 bits @ 150 MHz Display Data
Partial Reconfiguration Region
8 bits @ 150 MHz Compressed Data
– External Source
Notes: Customer can service two incoming video data formats in one FPGA, and swap decoding algorithms per port on the fly without disturbing the other port.
Hardware was initially released with service for two protocols, but is being updated for expanded service simply by uploading new bit files.

## Slide 12: Customer Example Sequential Processing
Automatic Fingerprint Authentication System
  Sequence of 12 different functions required
  No two were needed at any one time
Load in functions on demand
  Steps could be skipped or revisited
Processing time greatly improved
  PC-based Software solution: 3.77 sec
  Xilinx MicroBlaze solution: 143.19 sec
  Xilinx Partial Reconfiguration: 0.7 sec
    Includes 10ms total for all reconfiguration events
Efficient use of resources
  “Flat” solution requires 39k flops, 52k LUTs
  PR solution uses region with less than 10k of each
Read the detailed article in Xcell Issue 72

## Slide 13: Customer Example Fast PCIe Configuration and Field Updates
Customer requirements:
  Reduce PROM size
  Improve PCIe configuration time
  Enable live field updates
Solution details:
  Config time reduced 73%
  Static logic includes:
    PCIe Gen2x1 core
    Two 10G XAUI cores
    AXI debug logic
    ICAP loader

## Slide 14: Customer Example Hardware Acceleration
Dyplo = DYnamic Process LOader
  Solution distributes software functions between hardware and software spaces
Dyplo’s unique selling points
  Optimized use of Zynq SoC device
  Software driven Hardware development approach
  Abstraction of implementation choices to system level
  Simple use of partial reconfiguration blocks in hardware
  Configuration Wizard tool to guarantee ease of use
Product launched in March 2015
  Read more at http://topic.nl/en/dyplo or Xcell issue 85

## Slide 15: Outline
What is Partial Reconfiguration(PR)?
PR Technology
PR Terminology
PR Design Flow
Summary

## Slide 16: Programmability 101
Think of an FPGA as two layered device:
  Configuration memory layer
  Logic layer
Configuration memory controls function computed on logic layer
Configuration Memory Layer
Logic Layer

## Slide 17: “Normal” Configuration
Check Sum
Config. Data
Header
FPGA
Start
Vcc Rise
Vcc
Stable
Power-on
Reset
Configure
FPGA
Configuration Bitstream
User
Mode

## Slide 18: ‘Typical’ Configuration Mode
Fixed configuration
  Data loads from PROM or other source at power on
  Configuration fixed until the end of the FPGA duty cycle
Used extensively during traditional design flow
  Evaluate functionality of design as it is developed
Function
Power On
Shut
Down
Time
Configuration
Overhead
Device
Duty-cycle

## Slide 19: Reconfiguration
Configuration memory is no longer fixed during the system duty cycle
Initial bitstream loaded at power-on
Different, full device bitstreams loaded over time
Function
Configuration
Overhead
Reconfiguration
Overhead
Power On
Shut
Down
Time

## Slide 20: Partial Configuration
Config. Data
Start
Vcc Rise
Partial Configuration Bitstream
Initial Config.
Complete
Load Partial
Bitstream
FPGA
User
Mode
User
Mode

## Slide 21: Partial Reconfiguration
Only a subset of configuration data is altered
But all computation halts while modification is in progress…
Main benefit: reduced configuration overhead
Function
Configuration
Overhead
Reconfiguration
Overhead
Power On
Shut
Down
Time

## Slide 22: Dynamic Reconfiguration
A subset of the configuration data changes…
But logic layer continues operating while configuration layer is modified…
Configuration overhead limited to circuit that is changing…
Function
Configuration
Overhead
Reconfiguration
Overhead
Power On
Shut
Down
Time

## Slide 23: How Can We Reconfigure?
Initiation of reconfiguration is determined by the designer
  On-chip state machine, processor or other logic
  Off-chip microprocessor or other controller
Delivery of the partial bit file uses standard interfaces
  FPGA can be partially reconfigured through the SelectMap, Serial or JTAG configuration ports, or the Internal Configuration Access Port
Logic decoupling should be synchronized with the initiation and completion of partial reconfiguration
  Enable registers
  Issue local reset

## Slide 24: Outline
What is Partial Reconfiguration(PR)?
PR Technology
PR Terminology
PR Design Flow
Summary

## Slide 25: Hierarchical Implementation Definitions
Partition
  A logical block (entity or instance) to be used for design reuse
  User determines implementation versus preservation for each block
Bottom-up synthesis
  Separate synthesis projects resulting in multiple netlists or design checkpoints
  No optimization across projects
Top-down synthesis; NOT used for Partial Reconfiguration (normal flow)
  One synthesis project where synthesis flattens design for optimization
  Often called flat synthesis
  No support for hierarchical implementation

## Slide 26: Terminology
Reconfigurable Partition (RP)
  Design hierarchy instance marked by the user for reconfiguration
Reconfigurable Module (RM)
  Portion of the logical design that occupies the Reconfigurable Partition
  Each RP may have multiple Reconfigurable Modules
Static Logic
  All logic in the design that is not reconfigurable
Configuration
  A full design consisting of Static Logic and one Reconfigurable Module for each Reconfigurable Partition
Partition Pins
  Ports on a Partition; Interface between Static and Reconfigurable Logic

## Slide 27: Configurations
A Configuration is a complete FPGA design
  Consists of Static Logic and one variant for each reconfigurable instance
Maximum number of RMs for any RP determines minimum number of Configurations required
  Example: Possible Configurations for this design
    Static + A1 + B1 + C1
    Static + A2 + B2 + C2
    Static + A3 + B2 + C3
    Static + A3 + B2 + C4
  Static Logic and repeated RMs are imported
  Any combination of RMs can be selected to create unique full bit files
RP “A”
Static
RP “B”
RP “C”
A1
A2
A3
B1
B2
C1
C2
C3
C4
Reconfigurable Modules
Notes: How many bit files will be created in this example? 16. Each configuration will generate 1 full and 3 partial bit files.
How many unique bit files will be created? 13. There will be 2 for A3 and 3 for B2, but they will have different names.

## Slide 28: Reconfigurable Elements
What is reconfigurable?
  Nearly everything in the FPGA
    Slice logic (LUTs, flip-flops, and carry logic, for example)
    Memories (block RAM, distributed RAM, shift register LUTs)
    DSP blocks
Logic that must remain in static logic includes
  Clock-modifying blocks (MMCM, DCM, PLL, PMCD)
  Global clock buffers (BUFG)
  Device feature blocks (BSCAN, ICAP, STARTUP, or PCIE, for example)
  I/O components (IOLOGIC, IODELAY, IDELAYCTRL)

## Slide 29: Reconfigurable Elements
Granularity of reconfigurable regions vary by device family
  Boundaries recommended, but not required, to align to Clock Regions
  7-Series (Vivado/ISE supported)
    Slice region: 50 CLB high by 1 CLB wide
    BRAM region: 10 RAMB36
    DSP region: 20 DSP48
  Virtex-6 (ISE supported)
    Slice region: 40 CLB high by 1 CLB wide
    BRAM region: 8 RAMB36
    DSP region: 16 DSP48
  Virtex-5 examples (ISE supported)
    Slice region: 20 CLB high by 1 CLB wide
    BRAM region: 4 RAMB36
    DSP region: 8 DSP48
  Virtex-4 examples (ISE supported)
    Slice region: 16 CLB high by 1 CLB wide
    BRAM region: 4 RAMB16 and 4 FIFO16
    DSP region: 8 DSP48
  Bit file sizes for each of these resource types will vary

## Slide 30: Outline
What is Partial Reconfiguration(PR)?
PR Technology
PR Terminology
PR Design Flow
Summary

## Slide 31: Intuitive Design Flow Project Creation and Floorplanning
Structure your design
  Static Logic (unchanging design)
  Reconfigurable Partitions (RP)
    Instances to be reconfigured
  Reconfigurable Modules (RM)
    Functional variations for each RP
Synthesize bottom-up
  synth_design –mode out_of_context
Define resources to be reconfigured
  Pblocks map design modules to physical regions
    Define XY ranges and resource types
Mark pblocks as reconfigurable
  HD.RECONFIGURABLE initiates flow
Static Logic
RP_color
RP_pos
RM_orig
RM_rev
RM_allc
RM_gray
RM_sepia
i_PR_color
i_PR_pos

## Slide 32: Leveraging Module Checkpoints for Partial Reconfiguration
Partition methodology enables Partial Reconfiguration
  Allows clear separation of static logic and Reconfigurable Modules
  Floorplan to identify silicon resources to be reconfigured
Design preservation accelerates design closure
  Lock static design database while implementing new modules
Partitioning, Floorplanning
RP_color
RP_pos
RM_orig
RM_rev
RM_allc
RM_gray
RM_sepia
Static Logic
Static Logic
RP_color
RP_pos
Implementing Configuration
RM_orig
RM_allc
STATIC
Storing Results
To Implement Next Configuration
RM_gray
STATIC
RM_rev
Implementing Configuration
Storing New Results
import
implement
implement
preserved
implemented
implemented

## Slide 33: Vivado Software Features No Proxy Logic Required
Partition Pins are junction between static and reconfigured logic
  Interface wires can be broken at interconnect tile site
  “Anchor” between static and reconfigurable established mid-route
  No overhead at reconfigurable partition interface
  Decoupling logic still highly recommended
INT tile

## Slide 34: Vivado Software Design Management Checkpoints for Each Partition
static.dcp
BB
BB
RP_1
RP_2
Vivado stores design data in checkpoints
  Save full design as a configuration checkpoint for bitstream creation
  Save static-only checkpoint to be reused across multiple configurations
    Routed static checkpoint can remain open in memory
    Results are locked at the routing level
  Reconfigurable modules can also be stored as their own checkpoints
config_1.dcp
config_2.dcp
RM_1a.dcp
RM_2a.dcp
RP_1
RP_2
Load new synthesized modules to replace black boxes and create new configurations
Notes: For this example design:
config_1.dcp can be used to create config_1.bit (which is the full design including RM_1a and RM2a), RP_1.bit and RP_2.bit
config_2.dcp can be used to create config_2.bit (with empty modules for the two RPs), and black box versions of RP_1.bit and RP_2.bit
New modules can be loaded in over the black boxes to create new configurations

## Slide 35: Intuitive Design Flow Implementation
Place and Route all design configurations
  Apply full design constraints in-context
  Use normal timing closure, simulation and verification techniques
  Currently non-project Tcl flow only – sample scripts provided
Final Verification
  Validates consistency of place and routed results across the entire system
Generate Bitstreams
  write_bitstream automatically creates all full and partial bit files

## Slide 36: Configuration Details
Partial bit files are processed just like full bit files
  Bit file sizes will vary depending on region size and resource type
  Contain just address & data, sync & desync words, optionally final and frame-based CRC value
    No startup sequences, DONE flag
Partial Reconfiguration time depends on two factors:
  Configuration bandwidth
  Partial bit file size
    Estimate in Vivado, confirm in Rawbit file
Configuration Mode | Max Clock Rate | Data Width | Max Bandwidth
SelectMap / ICAP | 100 MHz | 32-bit | 3.2 Gbps
Serial Mode | 100 MHz | 1-bit | 100 Mbps
JTAG | 66 MHz | 1-bit | 66 Mbps

## Slide 37: Partial Reconfiguration Collateral
Learn about Partial Reconfiguration
  User Guide UG909
  Tutorial UG947
  PR Design Hub in DocNav
  XAPP1159
  More IP and references in the works
Read about Partial Reconfiguration
  Xcell articles in Issues 72, 73, 75, 77, 78, 79, 80, 84, 85

## Slide 38: Outline
What is Partial Reconfiguration(PR)?
PR Technology
PR Terminology
PR Design Flow
Summary

## Slide 39: Summary
Partial Reconfiguration is an Expert Flow
Understanding PR terminology provides a commonality for PR design communication
PR enables
  System flexibility
  Size and cost reduction
  Power reduction
The PR flow has four primary steps
  Set up the design structure
  Constrain RPs and run DRCs
  Place & Route configurations
  Create bit files