## Slide 1: Synthesis

## Slide 2: Objectives
After completing this module, you will be able to:
  Elaborate a design and perform analysis
  Make basic timing constraints with the Constraints viewer
  Use the check_timing report to verify constraint coverage of your design
  Build useful design reports that will help you avoid the most common design mistakes and assure design success
  Use the clock_interaction report to verify constraint coverage on datapaths between clock domains

## Slide 3: Outline
Elaboration
Synthesis
Basic Timing Constraints
Synthesis Reports
Summary

## Slide 4: Elaboration
Elaboration is the RTL optimization to an FPGA technology
Vivado IDE allows designers to import and manage RTL sources
  Verilog, System Verilog, VHDL, NGC, or testbenches
Create and modify sources with the RTL Editor
  Cross-selection between all the views
Sources view
  Hierarchy view: Display the modules in the design by hierarchy
  Libraries view: Display sources by category

## Slide 5: Elaboration and Analysis
In a RTL based design, elaboration is the first step
Click on Open Elaborated Design under RTL Analysis to
  Compile the RTL source files
  Load the RTL netlist for interactive analysis
You can check RTL structure, syntax, and logic definitions
Analysis and reporting capabilities include:
  RTL compilation validation and syntax checking
  Netlist and schematic exploration
  Design rule checks
  Early I/O pin planning using an RTL port list
  Ability to select an object in one view and cross probe to the object in other views, including instantiations and logic definitions within the RTL source files

## Slide 6: Analysis of an Elaborated Design
Three options available after opening an Elaborated Design
  Report DRC
    Runs DRC on the design
  Report Noise
    Checks the SSO on the design based on a XDC file
  Schematic
    Opens the schematic

## Slide 7: Schematic View of an Elaborated Design
When Schematic is clicked under the Elaborated Design, the schematic is opened showing the hierarchical blocks
  Note that no I/O buffers are inferred at this stage
  Each block opens up to reveal underlying logic and sub-modules in the hierarchy
  Closest representation to the actual coded design

## Slide 8: Cross Probing
Select an object in the schematic, right-click, and select Go To Source to view where the object is defined in the source file

## Slide 9: Outline
Elaboration
Synthesis
Basic Timing Constraints
Synthesis Reports
Summary

## Slide 10: Synthesis: Logic Optimization and Mapping to Device Primitives
Synthesis of an RTL design
  Optimizes the gate-level design
  Maps the netlist to Xilinx primitives
    Sometimes called technology mapping
The figure shows a generic FIFO behavioral component mapped to the dedicated FIFO hardware in a 7-Series FPGA
Notes: Getting behavioral logic to map to specific primitives may require specific HDL coding techniques or synthesis-specific primitives. Hopefully generic inference is sufficient, but it will depend on the architecture resource and the synthesis tool

## Slide 11: Vivado IDE Synthesis
Applicable only for RTL (HDL) design flows
  EDIF is black boxed and linked after synthesis
Synthesis tool uses XDC constraints to drive synthesis optimization
  XDC file must exist
Timing constraints considerations
  Design must first be synthesized without timing constraints for constraints editor usage
  Constraints Wizard is available after synthesis to define rudimentary timing constraints
Synthesis settings provide access to additional options
Note the changes in the Flow Navigator when the synthesized design has been opened
  Set Up Debug allows for integration of debug feature

## Slide 12: Vivado IDE Synthesis Settings
Synthesis Settings brings up Project Settings dialog box
  Central location for all project settings
Select the Default Constraint Set as the active constraint set. Two types of the design constraints
    Physical constraints define pin placement, and absolute, or relative, placement of cells such as block RAMs, LUTs, Flip-Flops, and device configuration settings.
    Timing constraints, written in industry standard SDC, define the frequency requirements for the design. Without timing constraints, the Vivado Design Suite optimizes the design solely for wire length and placement congestion.
Notes: Note that with improvements in elaboration, more improvements in synthesis can now be found. All synthesis options can be found under the Synthesis Settings options in the Vivado IDE GUI.

## Slide 13: Vivado IDE Synthesis Settings
The tcl.pre and tcl.post options are hooks for Tcl files that run immediately before and after synthesis
flatten_hierarchy: Determines how synthesis controls hierarchy
  none: Do not flatten the hierarchy.
    Maintains the exact same hierarchy as the original RTL
  full: Fully flatten the hierarchy leaving only the top level
  rebuilt: Flatten the hierarchy, perform synthesis, and then rebuild the hierarchy based on the original RTL
    Allows the QoR benefit of cross-boundary optimizations, with a final hierarchy that is similar to the RTL for ease of analysis
gated_clock_conversion: Turns on and off the synthesis tools ability to convert clock_logic with enables
Notes: Note that with improvements in elaboration, more improvements in synthesis can now be found. All synthesis options can be found under the Synthesis Settings options in the Vivado IDE GUI.
design_opt = logic trimming (used to be in Map).
synth_opt = logic optimization (fanout control, hierarchy opt, logic optimization, retiming, register balancing).
ower_opt = power optimization switches.

## Slide 14: Vivado IDE Synthesis Settings
bufg: Controls how many BUFGs the tool infers in the design
  This option is used when other BUFGs in netlists are not visible to the synthesis process
fsm_extraction: Encode the state machine in a specific encoding type: one_hot, sequential, johnson, gray, or auto
keep_equivalent_registers: Prevents registers with the same input logic from being merged
resource_sharing: Sets the sharing of arithmetic operators between different signals
  The values are auto, on and off
Notes: fsm_extraction: Controls how synthesis extracts and maps finite state machines. By default this option is set to off, and the state machine is synthesized as logic. Or you can choose from the following options to encode the state machine in a specific encoding type: one_hot, sequential, johnson, gray, or auto
Note that with improvements in elaboration, more improvements in synthesis can now be found. All synthesis options can be found under the Synthesis Settings options in the Vivado IDE GUI.
design_opt = logic trimming (used to be in Map).
synth_opt = logic optimization (fanout control, hierarchy opt, logic optimization, retiming, register balancing).
ower_opt = power optimization switches.

## Slide 15: Vivado IDE Synthesis Settings
control_set_opt_threshold: Sets the threshold for clock enable optimization to the lower number of control sets
no_lc: When checked, this option turns off LUT combining
shreg_min_size: Is the threshold for inference of SRLs
  This sets the number of sequential elements that would result in the inference of an SRL for fixed delay chains (static SRL)
max_bram: Limits the number of BRAM allowed in the design.
  -1 default lets the tool pick as many BRAM as it can, limited by number of BRAMs in device
max_dsp: Similar in concept to max_bram, except this applies to DSPs.
To see explanation of each option, click on the name of each option to highlight it.
Notes: control_set_opt_threshold: Sets the threshold for clock enable optimization to the lower number of control sets. The default is 1.
The given value is the number of fanouts necessary for the tool to move the control sets into the D logic of a register. If the fanout is higher than the value, the tool attempts to have that signal drive the control_set_pin on that register.

## Slide 16: Synthesis RTL Attributes Supported

## Slide 17: Synthesis RTL Attributes Supported, cont’d…

## Slide 18: Attributes Example in RTL
No support for timing constraints embedded in RTL
Example of KEEP attribute
VHDL
  signal sig1 : std_logic;
  attribute KEEP : string; attribute KEEP of sig1 : signal is "true";
  sig1 <= in1 and in2;
  out1 <= sig1 and in3;
Verilog
  (* KEEP = "true" *) wire sig1;
  assign sig1 = in1 & in2;
  assign out1 = sig1 & in3; // without the attribute sig1 will be optimized away if it not // being used anywhere else in the model

## Slide 19: Attributes Example in RTL
Attributes do not work with Verilog 2001 module syntax
Does Not Work
module top ((* buffer_type = "none" *) input sys_clock,
input sys_reset,
(* buffer_type = "none" *) input serDataIn,
Works
module top ( sys_clock,
sys_reset,
serDataIn,
…
);
(* buffer_type = "none" *) input sys_clock;
input sys_reset;
(* buffer_type = "none" *) input serDataIn;

## Slide 20: Mark_Debug RTL Attribute
MARK_DEBUG support with Vivado synthesis
  Tag signals in HDL
  Corresponding nets preserved in netlist (DONT_TOUCH behavior)
  Tagged nets appear in the logic analyzer Unassigned nets view
  XDC and elaborated design netlist support available
You can also mark nets after synthesis
After Synthesis
Apply attribute in HDL
Notes: MARK_DEBUG is an attribute designated for tagging signals for debug and it is now supported in Vivado IDE design flows. MARK_DEBUG can be applied in multiple ways depending on needs and design flows.
MARK_DEBUG attributes can be applied in HDL files and synthesized design netlists. Support for placement of MARK_DEBUG attributes in both XDC and elaborated design netlists is available.

## Slide 21: Outline
Elaboration
Synthesis
Basic Timing Constraints
Synthesis Reports
Summary

## Slide 22: Basic Timing Constraints
There are three basic timing constraints applicable to a sequential machine
  Period
    Paths between synchronous elements clocked by the reference clock net
      Synchronous elements include flip-flops, latches, synchronous RAM, and DSP slices
    Use create_clock to create the constraint
  Input Delay
    Paths between input pin and synchronous elements
    Use set_input_delay to create the constraint
  Output delay
    Paths between synchronous elements and output pin
    Use set_output_delay to create the constraint
More about this in the module on Xilinx Design Constraints

## Slide 23: Constraints Viewer
Constraints Viewer allows you to see/edit the timing constraints contents of the XDC file
  All timing constraints are supported with the GUI
  Right-clicking the constraint in the Create window allows you to modify/delete an existing constraint
  Select a different constraint by clicking it in the All Constraints window
  To create a different constraint, select the type from the GUI
After constraint entry is completed, constraints must be "saved" to have them stored in the XDC
  Changes will be written into the specified Target XDC only

## Slide 24: Creating Basic Timing Constraints in Vivado IDE
Run Synthesis
Open the synthesized design
Invoke constraints editor
Notes: This only works after synthesis. Launch the timing constraints menu by (1) clicking on Edit Timing Constraints, (2) double click on Create Clock. Optionally (but importantly) set the Input Delay by double clicking on the input delay option.

## Slide 25: Creating Basic Timing Constraints using Tcl
Period constraint using create_clock
  create_clock –period 10 [get_ports clk_pin]
  create_clock –period 10 –waveform {0.000 5.000} –name clk [get_ports clk_pin]
set_input_delay
  The input delay external to FPGA
  set_input_delay –clock clk_pin 2.000 [all_inputs]
  set_input_delay –clock clk_pin 3.000 [get_ports in1]
  set_input_delay –clock clk_pin 2 [get_ports l_msn* ]
set_output_delay
  The output delay external to FPGA
  set_output_delay –clock clk_pin -2 [all_output]
  set_output_delay –clock [get_clocks clk_pin] -2 [get_ports out1]
Notes: You need to first create the Period constraint to define a clock and a period (waveform is optional, see second line of constraints in example above).
After that, you can define input/output delays based on the defined period constraints.

## Slide 26: Timing Paths Example

## Slide 27: Constraints Wizard
Allows Vivado to suggest timing constraints missing from the design
  Recommended flow for an initially unconstrained design
  User can ignore the recommended constraints
    Option to deselect constraints at every stage of the wizard
  Opens the Timing Constraints Editor with recommended constraints
    User needs to consciously add the constraints to the target XDC file
  A great alternative to using the Timing Constraints Editor in Vivado
    User can still use the editor to add constraints
Notes: You need to first create the Period constraint to define a clock and a period (waveform is optional, see second line of constraints in example above).
After that, you can define input/output delays based on the defined period constraints.

## Slide 28: Outline
Elaboration
Synthesis
Basic Timing Constraints
Synthesis Reports
Summary

## Slide 29: After Synthesis
In the Synthesized Design view:
Sources tab does not change
  RTL Netlist tab (Elaborated Design) changes to Netlist (Synthesized Design)
However, the Flow Navigator now includes:
  Constraints Wizard, Edit Timing Constraints, Set Up Debug, Report Timing Summary, Report Clock Networks, Report Clock Interaction, Report DRC, Report Noise, Report Utilization, Report Power, Schematic
Views can selected by purpose
  All timing information is only an estimate (until implementation has completed)
  Setup debug tool

## Slide 30: Synthesized Design
Accessed through the Flow Navigator by selecting Open Synthesized Design
Representation of the design after synthesis
  Interconnected netlist of hierarchical and BELs
    Instances of modules/entities
    BELs
      LUTs, flip-flops, carry chain elements, wide MUXes
      Block RAMs, DSP cells
      Clocking elements (BUFG, BUFR, MMCM, …)
      I/O elements (IBUF, OBUF, I/O flip-flops)
Object names are the same as names in the elaborated netlist when possible

## Slide 31: Synthesis Reports
While the Flow Navigator points to the most important reports, the Reports tab contains several other useful reports
  Vivado Synthesis Report shows
    HDL files synthesized, synthesis progress, timing constraints read, and RTL primitives from the RTL design
    Timing optimization goals, technology mapping, removed pins/ports, and final cell usage (technology-mapped cell usage)
  Utilization Report shows
    Technology-mapped cell usage in an easy-to-read tabular format

## Slide 32: Synthesis Utilization Report
Reports slice logic, memory, DSP slice, IO, clocking, and other resources used by the design

## Slide 33: Commands Available After Synthesis
Flow Navigator is optimized to provide quick access to the options most frequently used after synthesis
  Constraints Wizard: Already mentioned
  Edit Timing Constraints: Launch the timing constraints tab
  Set Up Debug: Launch the view for marking nets for debug
  Report Timing Summary: Generate a default timing report
  Report Clock Networks: Generates a clock tree for the design
  Report Clock Interaction: Verifies constraint coverage on paths between clock domains
  Report DRC: Performs design rule check on the entire design
  Report Noise: Performs an SSO analysis of output and bidirectional pins in the design
  Report Utilization: Generates a graphical version of the Utilization Report
  Report Power: Detailed power analysis reports
  Schematic: Opens the Schematic viewer

## Slide 34: Report Timing Summary
Vivado IDE
Options tab
  Maximum number of paths
Advanced tab
  Write to a file
Timer Settings
  Interconnect delay can be ignored
  Flight delays can be disabled
Tcl command: report_timing_summary
report_timing_summary -delay_type max -report_unconstrained -check_timing_verbose -max_paths 10 -input_pins -name timing_1

## Slide 35: Report Timing Summary
Design Timing Summary
  WNS, TNS, total number of endpoints are of interest
Clock Summary
  Primary and derived clocks
Check Timing
  Number of unconstrained internal endpoints

## Slide 36: Report Clock Networks
To generate a report on the clock networks in a design, use the tcl command
  report_clock_networks
  Creates a tree view of all the logical clock trees found in the design, annotated with existing and missing clock definitions on the roots of these trees
Vivado IDE

## Slide 37: Report Clock Interaction
Use Tcl command
  report_clock_interaction -significant_digits 3 -name timing_1
Reports paths on inter-clock domain paths and unclocked registers
  Uses an inter-clock path matrix to show clock relationships and group paths
  Tells if timing is asynchronous and if paths are constrained (green)
  Uses the worst-slack value for each clock grouping

## Slide 38: Report DRC
Use Tcl command
  report_drc -name drc_1
DRCs performed early in the design flow allow for correction before a full implementation
  Objects listed in violations are cross-selectable with HDL sources
  Can select which DRCs to run, or run all
    This check is more thorough than the I/O DRC checks that occur during pin planning
  Any problems will open a DRC window at the bottom of the GUI
  Run implementation for the final sign-off DRC
Vivado IDE

## Slide 39: Report Noise
Use Tcl command
  report_ssn -name ssn_1
Performs a SSN analysis of the planned I/O layout
  This report is looking to gauge the number of pins, I/O standard, and drive strength on a bank-by-bank basis
    Banks that exceed what is recommended will be flagged in the Summary tab
    SSN analysis can only be done on output and bidirectional ports
Vivado IDE

## Slide 40: Report Power
Use Tcl command
  report_power -results {power_1}
Accurate power and thermal analysis
Power estimates at every stage after synthesis
Perform what-if analysis by varying switching activity
Extensive debug capabilities through cross-probing
Exports data to XPE

## Slide 41: Power Utilization Details
Select different resource types to see more details

## Slide 42: Outline
Elaboration
Synthesis
Basic Timing Constraints
Synthesis Reports
Summary

## Slide 43: Summary
Elaborated design allows early drc checks, noise analysis, and cross-probing between the source file and the generated hierarchical design
Synthesis performs logic optimization and technology mapping to Xilinx primitives
Vivado IDE supports VHDL, Verilog, and SystemVerilog
Vivado IDE supports the use of Xilinx Design Constraint (XDC) syntax, which is used to drive synthesis design optimization
check_timing report is used to verify that a design has been sufficiently constrained by the designer
Vivado IDE includes numerous reporting mechanisms for the designer to improve performance, avoid common design mistakes, and get the most out of the FPGA